Lab 5 Projectile motion

Object: Examine the kinematics of 2-D projectile motion

Apparatus:

USB Scientific workshop interface; Two photogates; Projectile launcher; Meters

Theory

The kinematics of the projectile motion, if ignoring the air resistance force and variation of gravity, can described by the following 2-D motion equation:

y = y0 + vi sinθ t + ½ g t2     and    x = x0 + vi cosθ t

where x is the position in horizontal direction and y is the position in vertical direction, g is the gravity constant,  θ is the launch angle. From the kinematics equations, we can find the projectile flight distance d,

d = vi2*sin(2θ) / g

Procedure:

- Turn on iMac computer

- Turn on Scientific workshop interface

- Attach two photogates to the projectile launcher

- Measure the distance between the two photogates. Adjust the distance parameter used by DataStudio™ to calculate the speed.

- Connect the outputs of the two photogates to the digital input of Scientific workshop interface

- Adjust the angle of the projectile launcher. Record the launching angle.

- The plastic rod to load the plastic ball into the projectile launcher

- Launch the plastic ball by pulling the yellow firing string.

- Locate the point that the plastic ball hit the floor and record the distance from the launcher to the landing point.

- Repeat step 7-9 5 times for each difference angles.

Results

Table I

Launch Angle                  Trial                 vi                        dexp                           dcalc                   percentage error

1

2

Angle 1                        3

4

5

1

2

Angle  2                       3

4

5

Question;

1. Draw the distance vs. (square of initial velocity) plot. Explain the deviation from the linear relation predicted by theory.