# Specific Heat of an Unknown Metal

| Thermodynamics: specific heat, calorimetry, thermal energy |  |
| --- | --- |

| Qty | Equipment and Materials | Part Number |
| --- | --- | --- |
| 1 | PASPORT Xplorer GLX | PS-2002 |
| 1 | Fast-Response Temperature Probe (included with GLX) |  |
| 1 | Basic Calorimetry Set (1 metal object and 2 calorimeter cups) | TD-8557 |
| 1 | Balance | SE-8723 |
| 1 | Graduated Cylinder, 50-mL | SE-7289 |
| 20 cm | Braided Physics String | SE-8050 |
| 1 | Stir rod |  |
| 300 mL | Water |  |
| 100 mL | Ice (cube or crushed) |  |
| 1 | Towel |  |

## Purpose

## The purpose of this activity is to determine the specific heat of a metal object and identity the metal based on its specific heat.

## Background

## The amount of thermal energy that an object must absorb to change its temperature by one degree is called its heat capacity. The amount of thermal energy that a single gram of a specific material must absorb in order to change its temperature by one degree is the material's specific heat capacity, or specific heat. The specific heat of water is a standard to which specific heats of other substances are compared.

## When thermal energy flows into or out of an object, its temperature changes. The amount of change depends on the mass of the object, the material from which the object is made, and the temperature of the environment. The specific heat of the material can be found using a known quantity of water and a calorimeter. The calorimeter is relatively well insulated so very little thermal energy will come from or go into the surrounding air. Assume that thermal energy is conserved inside the calorimeter. This means that whatever thermal energy is gained or lost by an object put into the calorimeter is equal to the thermal energy gained or lost by the water in the calorimeter. The equation describes that the change in thermal energy, ∆Q, depends on the mass, m, the specific heat, c, and the change in temperature, ∆T.

When an unknown metal object is put into water in a calorimeter, the change in thermal energy of the object equals the change of thermal energy of the water.

The initial temperatures of the object and water will be different, but the final temperature–called the equilibrium temperature–will be the same.

## Preview

## Use a Fast-Response Temperature Probe to measure the change in temperature of a known mass of water at room temperature when a metal object of known mass and known initial temperature is put into the water. Use the Xplorer to record and display the data.

## Safety Precaution

Follow all directions for using the equipment.

## Procedure

### GLX Setup

- Plug a Fast-Response Temperature Probe into the first temperature port  on the left side of the Xplorer GLX and then turn on the GLX ().

The Graph screen shows Temperature (ºC) and Time (s).

### Equipment Setup

- Measure and record the mass of one of the metal objects from the PASCO Basic Calorimetry Set.

- Put ice and water into one calorimeter cup to make an ice water bath. Tie a piece of string to the metal object and lower the object into the ice bath.

- Leave the metal object in the ice water for 10 minutes. Add more ice as the ice begins to melt.

- Prepare a known quantity of water that is at room temperature (about 20–25 ºC). Measure and record the mass of the second calorimeter cup. Add about 200 mL of water to the calorimeter. Measure and record the total mass of the cup plus the water.

- Put the end of the Fast-Response Temperature Probe into the room temperature water. Add a stir rod to the water.

### Record Data

- Press Start () on the GLX to measure the signal from the Temperature Probe.

The temperature appears in the graph display.

- After 1 minute, lift the cold metal object out of the ice water bath and quickly dry any droplets of water still on the object.

- Suspend the object in the room temperature water in the calorimeter. It should be completely covered by water but not touch the bottom of the calorimeter.

- Stir the water gently as you continue to record temperature data.

- Wait until the graph of temperature stops changing (the object and the water are in thermal equilibrium), and then press  to stop data recording.

- Remove the Temperature Probe and the metal object from the calorimeter. Clean up the equipment as instructed.

## Analysis

Use the graph of temperature versus time to find the initial temperature of the water and the equilibrium temperature, or final temperature, of the water and the metal object after the object warms up and the water cools down.

Press F3 () to open the Tools menu. Select Smart Tool. Use the arrow keys to move the cursor to the part of the graph that shows the initial temperature of the water. Record the value.

Repeat the process to find the final temperature (equilibrium temperature) of the water and the metal object.

Use your data to calculate the specific heat of the metal object.

Use your calculated value of the specific heat to identify the type of metal.

### Record your results and answer the questions in the Lab Report.

## Extension

Repeat the procedure with the other metal objects in the Basic Calorimetry Set.

## Lab Report - Activity 31: Specific Heat of an Unknown Metal

## Name ________________________________ Date ___________

## Data

Sketch your graph of temperature versus time. Include labels and units on the axes.

## Data Table

| Item | Value |
| --- | --- |
| Mass of object | kg |
| Mass of cup | kg |
| Mass of cup plus water | kg |
| Mass of water | kg |
| Initial Temperature of Metal | 0 ºC |
| Initial Temperature of Water | ºC |
| Final Temperature of Water | ºC |

## Calculations

Calculate the specific heat of the unknown metal. The specific heat of water, cwater is 4186 J/kg˚C. Remember that the final temperature of the water–the equilibrium temperature–is also the final temperature of the metal object. Assume that the initial temperature of the metal object is 0ºC (the temperature of the ice-water bath).

Solve for the specific heat of the object, cobject.

| Item | Value |
| --- | --- |
| Specific Heat of Metal | J/kg˚C |

The table shows some specific heats of common metals:

| Metal | Specific Heat (J/kg˚C) | Metal | Specific Heat (J/kg˚C) |
| --- | --- | --- | --- |
| aluminum | 901 | iron | 449 |
| brass | 380 | lead | 128 |
| copper | 386 | silver | 234 |
| gold | 129 | steel | 450 |

## Questions

- Describe, in words, what happened to the temperature on the graph.

- What kind of metal is the object?

- Compare the value you obtained with your data (measured) to the value in the list (accepted). For example, what is the percent difference between your measured value and the accepted value?

- What are some possible sources of error?

# Text boxes

Fig. 2: Equipment setup

Fig. 1: GLX graph